## Slide 1
Core Facility for Cell Sorting and Cell Analysis
What is wrong with my flow cytometry data?
Hints, tricks and pitfalls

## Slide 2
2
Webinar 6
04.07.2023
When to use which buffer system

## Slide 3: What we need to talk about…
Core Facility for Cell Sorting and Cell Analysis
3
Staining protocol
  Surface vs. intracellular vs. intranuclear
Cell Staining buffer
Blocking buffer
Perm buffer
Fixation buffer
Special
  RBC lysis buffer
  Annexin Binding buffer
  Cell cycle buffer

## Slide 4: Staining strategies: what are you looking for
Core Facility for Cell Sorting and Cell Analysis
4
https://www.ptglab.com/media/5016/flow-cytometry-7.png?width=585px&height=391px

## Slide 5: Simple staining buffer for surface staining
Self-made
1X PBS (w/o Mg2+, Ca2+ )
  + 1-2% BSA / FCS (heat-inactivated)
  + 2-5 mM EDTA
  + 2mM NaN3 or 1% Pen/Strep
serum and EDTA concentrations depend on tendency of cells to aggregate
Commercial
Miltenyi autoMACS Running Buffer (BSA, EDTA, Acid) # 130-091-221
Miltenyi autoMACS Rinsing solution (EDTA) , # 130-091-222
BioLegend Cell Staining buffer, # 420201
Core Facility for Cell Sorting and Cell Analysis
5

## Slide 6: Blocking: not just an issues of Fc receptors
Self-made to block FcR
10% BSA/FCS in cell staining buffer
5-10 min on ice prior or simultanously with antibody incubation
Core Facility for Cell Sorting and Cell Analysis
6
Human TruStain FcX™ treated (blue) or non-treated (red) THP-1 cells stained with an irrelevant mouse IgG2a PE mAb (above). Dotted histogram represents unstained cells
https://d1spbj2x7qk4bg.cloudfront.net/Admin/Public/GetImage.ashx?Image=/Files/Images/media_assets/products/product_images/HumanTruStainFcX_100517.png&Width=240&Height=300&altFmImage_path=&Compression=90&Crop=5
BALB/c splenocytes were incubated with TruStain FcX™ PLUS (clone S17011E, 0.25µg/106 cells, filled histogram) or TruStain FcX™ (clone 93, 1µg/106 cells, red line histogram) to block the Fc receptors, or were left untreated (black line histogram); then stained with CD90.2 (Thy-1.2, clone 53-2.1) FITC. Note the high background in the untreated cells and the bigger reduction in the background staining when the cells were incubated with TruStain FcX™ Plus compared to TruStain FcX™.
https://d1spbj2x7qk4bg.cloudfront.net/Admin/Public/GetImage.ashx?Image=/Files/Images/media_assets/products/product_images/TruStain_FcX_Plus_CD16-CD32_Antibody_122018_updated.png&Width=240&Height=300&altFmImage_path=&Compression=90&Crop=5
Commercial
BioLegend TrueStain FcX PLUS (anti-mouse CD16/32)
  α- CD16/32 blocking non-specific binding of Ig to Fc receptors
BioLegend Human TrueStain FcX
  specialized human IgG binding to various Fc receptors via Fc portion

## Slide 7: Blocking: not just an issues of Fc receptors
Core Facility for Cell Sorting and Cell Analysis
7
Non-specific binding of monocytes to fluorophors (esp. tandems)
Biolegend True-Stain Monocyte Blocker
Miltenyi Human Tandem Signal Enhancer
https://www.bdbiosciences.com/content/dam/bdb/products/global/reagents/flow-cytometry-reagents/research-reagents/buffers-and-supporting-reagents-ruo/563794_base/BD_Horizon_Brilliant_Stain_Buffer_Figure.png
https://www.biolegend.com/Files/Images/BioLegend/monocyte_blocker/MonoBlock_Fig1a.jpg
BD Brilliant Stain Buffer minimizes fluorophor interaction which might cause staining artifacts

## Slide 8: Fixation: prior and/or after surface staining
~4-5% formaldehyd or paraformaldehyd or in combination with methanol
might reduce fluorophor intensity or even degrade tandem dyes
  BioLegend Fluorofix Buffer (4h storage, afterwards in cell staining buffer)
might demask/denature epitope
commercially often in set with perm buffer
Core Facility for Cell Sorting and Cell Analysis
8

## Slide 9: Intracellular staining: permeabilization
fresh PBMCs IFN-a stimulated (filled) vs. untreated (open)
for cytokine and chemokine staining (FA-, saponin based):
  BD Cytofix/Cytoperm Fix/Perm Solution
  BioLegend Cyto-Fast Fix/Perm Buffer Set
  BioLegend Intracellular Staining Perm/Wash Buffer 10X
https://www.bdbiosciences.com/content/dam/bdb/products/global/reagents/cell-preparation-separation-reagents/blood-lysis/staining-and-cell-preparation/558050_base/558050_image_1.png
pSTAT6
https://www.biolegend.com/en-gb/products/true-phos-perm-buffer-12691?GroupID=GROUP22
human lymphos IL-4 stimulated (filled) or unstim (open)
9
Human whole blood was stimulated with (right) or without (left) IL-6 for 15 minutes, then treated with RBC/Lysis Fixation Solution and permeabilized with True-Phos™ Perm Buffer
pSTAT3
CD3
for phospho-proteins (methanol-based)
  BioLegend True-Phos Perm Buffer
    not compatible with all cell surface markers!
    Recomm.: surface staining afterwards
  BD Phosflow Perm Buffer III
  -20°C or on ice
always dilute antibodies in perm buffer

## Slide 10: Intranuclear staining: permeabilization
for nucleus proteins harsh fix/perm:
  FA Fixation
  BioLegend True-Nuclear Transcription Factor buffer set: Saponin-based perm
    fix (~ 20% FA): step 45-60min at RT
    perm/wash (saponin)
    30 min RT incubation with intranuclear antibody at RT in perm buffer
  BD Transcription Factor Buffer Set
    fix/perm (5-10% FA, 1-3% methanol): step 40-50 min at 2-8°C
    perm/wash (saponin):
    40-50 min incubation with intranuclear antibody at 2-8°C in perm buffer
  choice of buffers depends on surface staining fluorophors
10

## Slide 11: Tandem dye stability upon fixation
Fix: 4,2 % FA
Perm/Wash: Saponin
Fix/Perm: 5% FA
Perm/Wash: 1-3% Methanol
Perm: 88% Methanol
from BD PhosFlow Kit
https://www.biolegend.com/Files/Images/BioLegend/blog/052418tandemblog/Figure_2.jpg
Cy5.5
Cy5.5
11

## Slide 12: Special buffers: functional assays, a.s.f.
Core Facility for Cell Sorting and Cell Analysis
12
RBC lysis buffer (self-made)
1,5 M NH4Cl 100 mM NaHCO3 oder KHCO3 10 mM EDTA pH 7,4 fill up to 1 L with AquaDest
AnnexinV binding buffer
AnnexinV is Calcium-dependent
incubation at RT
10 mM HEPES, pH 7,4 140 mM NaCl 2,5 mM CaCl2
Cell cycle
30 min ati RT in the dark or o.n. at 4°C
1 x PBS 0,1 % (w/v) Triton-X 10 µg/mL RNAse 20 µg/mL PI

## Slide 13: Buffer choice: Take home message
Core Facility for Cell Sorting and Cell Analysis
13
check target localization (surface, cytoplasmatic, intranuclear) and select correct buffer system
check fluorophor fixation stability
check target fixation stability
  https://www.biolegend.com/fixation

## Slide 14: Thank you for your attention. See you next month: 1st August Next topic The golden rules of panel design
Core Facility for Cell Sorting and Cell Analysis